## Slide 1: Introduction to Arduino
By Gabriel Unger

## Slide 2: What is Arduino?
Open-source physical computing platform
Atmel AVR ATmega microcontrollers
Free, simple IDE with built-in functions
Arduino Programming Language (C/C++)

## Slide 3: What is Arduino Used For?
Standalone systems
  Robots
  Pervasive computing (smart home)
Interface between physical world and computing world
  Our project
  Transducers feed Arduino
  Arduino feeds a system

## Slide 4: Why Arduino?
Easy
  Pre-made official boards
  C/C++
Open
  Third-party boards
  “Shields” extend functionality
Popular
  Community-developed libraries
  Online support community

## Slide 5: What Can Arduino Do?
Processing and Storage
  Capable processor (robot brain)
  SRAM, EEPROM, SD
Connectivity
  Basic digital, analog I/O
  Serial
  Bluetooth
  WiFi
  Zigbee
  NFC/RFID
  Ethernet

## Slide 6: Programming an Arduino Board
Arduino IDE
  Version 1.0
  Free
  C/C++
  “Sketches”
    One or more programs
    .ino extension
    setup() and loop()
Any other IDE
  Must support ATmega
  Few advantages

## Slide 7: Arduino Uno
Latest official Arduino board
ATmega328
  8-bit
  14 digital I/O (6 PWM)
  6 analog inputs
  16 MHz
  5V
  32 KB of program memory
  2 KB of SRAM (variables)
  1 KB EEPROM
  Serial port
  SPI port
  2 external interrupts
  AREF

## Slide 8: How Arduino Fits Our Project

## Slide 9: Analog Front End (AFE)
Grabs raw sensor outputs
  Voltages
  Currents
Provides data to next level of processing
Some provide advanced features
  Fundamental frequency
  Harmonic power
  Power factor

## Slide 10: Maxim AFE Devices

## Slide 11: MAXQ3183 Overview
3-Phase voltage, current
~$20 direct from Maxim
TSSOP (tiny)
SPI
3.3V
35 mW typical
7.6 MHz internal clock

## Slide 12: MAXQ3183 Internals